## Slide 1: Allen Brain Observatory Dataset
Madineh Sedigh-Sarvestani
CNI JC @ Upenn
Oct 2016
[Most slides are from Allen Institute’s Marina Garrett, or the Observatory website [observatory.brain-map.org/]

## Slide 2: A ‘Window’ into the Brain
Mouse Brain

## Slide 4
Awake, head-fixed mice, looking at visual stimuli.
2P calcium fluorescence responses of hundreds of neurons.
+ running speed
Eye video
Mouse behavior

## Slide 5: Genetic tools (Cre-lines x GCamp) are used to make specific cell types glow. Observatory dataset uses mice from 4 cre-lines (all exc). 7 more (exc/inh) planned for release.

## Slide 6: A Rich Dataset
4 Visual areas
4 cre-lines

## Slide 7: A Rich, Standardized, Dataset
Quality control throws out bad data

## Slide 8: 2P Data Generation
Motion correction
Segmentation (find cells)
Registration (match cells)
Fluorescence extraction
Background subtraction
Data pre-processing (temporal alignment, etc)
Compute df/f
Compute stimulus-specific response features
All raw (pre-processed) data also available.
Notes: If you’ve done imaging, you know that this pipeline takes a fair amount of time to setup in your lab. And there is by no means consensus on what he best algorithms are to find the region of interest and how to subtract neuropil responses. But these are done for you here. And you have access to all levels of the data, from completely raw fluorescence traces without motion correction to each cell’s orientation selectivity index.

## Slide 9: Pre-calculated Response Features
Stimuli, shown in three 1 hour sessions
Receptive field
Response reliability for each stimulus type
Orientation/direction selectivity
Preferred: tf, sf, orientation, natural image frame
Modulating by running

## Slide 10: You can access some of the data (meta-data and extracted features) from the web. The rest (raw, post-processed, features) are accessible through a python package.

## Slide 11: Accessing the Data (Web)
Web: observatory.brain-map.org

## Slide 12: Data Format
Neurodata Without Borders (NWB).
  HDF5 file
  Includes stimulus data and metadata
Used for CRCNS ephys data sets:
  https://crcns.org/
This paper has code snippets for reading;writing NWB data into matlab or python:

## Slide 13
AllenSDK python package (toolbox) for downloading raw and processed data
Start with this example jupyter notebook
Accessing the Data (Python)

## Slide 14: A Jupyter/Python notebook is just a web app that lets you interactively run python code, and look at the output. http://jupyter.org/

## Slide 15
Run the notebook interactively (binder)
Accessing the Data (Python)

## Slide 16: What do to with all this data? You could: 1) benchmark various motion correction/spike-extraction algorithms 2) Validate previous work on bigger dataset 3) Test new theories (running?) 4) Use it for teaching

## Slide 17: Observatory Data Not Good for:
High temporal resolution (Calcium imaging)
  Imaging frame rate is 30 Hz
Anything with precise spatial location
  Eye movement (1/4 RF width) not controlled for until future release

## Slide 18: Observatory Data Good for:
Response variability with: areas, cre-lines, layers, running, pupil diameter (extract)
Modeling signal and noise variability with brain state (Scholvinck 2015+)
Encoding with correlations (Pillow 2008+)
  Also as a function of tuning similarity (sign-rule?)
Decoding with correlations
  Does shuffling trials reduce performance?

## Slide 19: Population Coupling: an invariant neuronal property?
Pop coupling: correlation between each cell’s activity and total population activity.
PC is peak of the spike-triggered population rate (stPR)
Okun et al. Nature 521 (511-15), 2015
Okun et al. Figure 1
Notes: Only use cells stable across all three sessions.
But define population as all cells in frame.

## Slide 20
strong
weak
~Soloists
~Choristers
Rows (cells) sorted by mean PC
PC low and invariant
PC high and invariant
Notes: Rows sorted by mean pc

## Slide 21: Slides and Jupyter notebook: https://github.com/msarvestani/CNI-JC
Much More info on Observatory: http://observatory.brain-map.org/

## Slide 22: Cre-lines

## Slide 23: GCaMPf6f (Chen 2013)